## Slide 1: Simulation of Potential Mobility of Contaminant Plumes
Prepared for
Sacramento Central Groundwater Authority
July 13, 2011

## Slide 2: Project Objective
Use the SacIWRM Particle Tracking Module (PTM) to simulate the temporal and spatial movement of regional contamination plumes for a 105-year hydrologic period
Regional contamination plumes simulated:
  Aerojet
  Boeing
  McClellan
  Mather
  Sacramento Downtown Railyard

## Slide 3: Project Approach
  Collect data & update the SacIWRM model as needed
  Use PTM to track particles, conservatively representing contamination plumes

## Slide 5: Recent History of SacIGSM Baseline Model Development
North Area refinement, re-calibration, and baseline update in September 2007 (SGA)
Central Area and South Area refinement & re-calibration in June 2008 (TNC)
Central Area baseline update in January 2009 (SCGA)
South Area baseline update in April 2009 (RBI)
Update of Remediation Operations June 2010 (SGA & SCGA)

## Slide 6: Baseline Model Assumptions Land Use
Land use based on DWR Land Use Survey 2000 Sacramento County.
  Non-urban parcels converted to urban between 2000 and 2007 were urbanized for the model based on Sacramento County APN data.

## Slide 7: Water Use
Incorporates
  Groundwater
  Surface water
  Tailwater reuse
  Recycled water
Agricultural
  Crop type and soil/climate data – Model calculations
Municipal
  UWMP data and local data
  Calibrated assumptions for rural areas

## Slide 8: Remediation Operations Update
  SacIWRM was updated with data on planned future remediation operations for Aerojet, Boeing, and Mather
  Operations of McClellan reflected current level of remediation
  No remediation operations at the Railyard site

## Slide 9: Remediation Operations Simulated in SacIWRM

## Slide 10: Regional Contamination Plumes (Based on 2007 Data)

## Slide 13: Animation of Baseline Results

## Slide 14: Summary
10 Years
  No Aerojet or Boeing particles representing the plume have escaped into the SCGA production wells influence area
  1% of Mather particles representing the plume have escaped into the SCGA production wells influence area
105 Years
  1% of Aerojet particles representing the plume have escaped into the SCGA production wells influence area
  8% of Boeing particles representing the plume have escaped into the SCGA production wells influence area
  19% of Mather particles representing the plume have escaped into the SCGA production wells influence area

## Slide 15: Relation to Mather Cleanup Work
Presentation given by AFRPA - May Board meeting
Differences due to scale (space and time)
SacIWRM – includes impacts of regional groundwater system
Mather –
  Model includes more detailed, local lithology
  Detailed concentration data
  Monitoring activities lead decision making
  Monitoring allows for ongoing optimization of cleanup

## Slide 16: Needed Coordination
Development activities
  New supply wells
  Preservation of monitoring network
Modeling
  Regional conditions  Local model boundaries
  Remediation pumping  Regional model
Cleanup progress updates
Element of GWMP: Control of the Migration and Remediation of Contaminated Groundwater

## Slide 17: Questions